## Slide 1: Organic Lab Equipment
Distillation
Reflux
Separating Funnel

## Slide 2
Water in
Water out
Product collecting
Heat
Distillation Apparatus
Anti-bumping granules
Liebig Condenser
Thermometer

## Slide 3
Heat Use a water bath … why?
Safety … no naked flames near organic solvents
Gentle … temperature cannot go above 100 oC . If higher temperatures used then organic molecules could decompose/oxidise

## Slide 4: Anti-bumping granules
Porcelain chips, or other inert material … why?
Prevents violent boiling
Liquid may be ejected out of the still-head into the condenser

## Slide 5: Thermometer
Gives exact temperature of vapour ie boiling point of material distilling over
2-methylpropan-2-ol bp 83 oC
2-chloro-2-methyl propane bp 52 oC
Drops condense on the thermometer then re-evaporate and go into the condenser

## Slide 6: Condenser
Water out
Water in
Hot gas in
Condensed liquid out
Why should the water flow be this way round?
Maximum heat transfer when coolant flows in opposite direction to the hot gases.
Prevents air bubbles accumulating and therefore reducing heat transfer through convection. Bubbles get swept away by the water current

## Slide 7: Reflux
Water in
Water out
No bung
Reaction mixture can be heated without losing volatile substances … they condense and run back down into the flask.
If a bung in the top there could be pressure build up and an explosion
Water does not flow counter-current to heat as the need to sweep out air bubbles is more important

## Slide 8: Separating Funnel
Least dense layer, usually organic
More dense layer, often aqueous
tap
bung
Hold tap and bung firmly when shaking
Take bung out when opening the tap

## Slide 9: Three necked flask